## Slide 1
EFPIA Workshop: Best Practices to minimize the occurrence of drug in biological samples from control animals
Brussels October 13th 2003

## Slide 2: Best Practices to minimize the occurrence of drug in biological samples from control animals
19 organisations represented
  7 CROs
  12 pharmaceutical companies
Senior toxicologist and bioanalyst representatives from each organisation
Expertise on GLP aspects of issue
  Industry – Kirk Huber
  Regulatory – Jurg Seiler (ToxiConSeil, ex Swissmedic)

## Slide 3: Programme
Introduction
Case studies, Dr Chris Powell, GSK
Is this a GLP issue? Dr Jurg Seiler
Two Breakout groups
  Toxicology procedures (including dispensary)
  Analytics (formulation and bio-specimens)
Facilitators
  Chris Powell (Toxicology)
  Kirk Huber (Analytics)
Rapporteurs
  Tim Gray (Toxicology)
  Susie Fowles (Analytics)
Plenary feedback from breakouts and next steps

## Slide 4: Next steps
Feedback from CPMP SWP, February 2004
Session at DIA Euro Meeting in Prague, March 2004
Publication in DIA journal
  Regulatory persepctive
  Case studies
  GLP asepcts
  Industry Workshop consensus reccomendations
  ?

## Slide 5: Toxicology breakout session feedback

## Slide 6: Dispensary: Test material receipt, identification and storage
Consensus recommendation
  Rigid container desirable; verify integrity of container; use double containment
  Weigh to start accountability
  Check C of A – adequacy, correspondence with label
  Label must provide unequivocal identification
    Eg. bar coding
    Both containers
  Store according to stability information
  Separation of control and test materials
    At least separate cupboard
Further action needed to reach consensus
  Shipping practice (and adequate identification documentation)
Comments
  Previous experience with this and related compounds
  Physicochemical properties

## Slide 7: Dispensary: Dose formulation procedures, identification, transport to animal room
Consensus recommendation
  Formulate control/vehicle in separate area (assumes proper cleaning procedures are in place)
  Formulate control/vehicle at separate time of day, control before test material
  Separate container of vehicle for dilution and for dosing
  Prepare formulations in ascending dose order
    Sample for analysis (TK days)
  Dispense formulations into unequivocally labelled containers
  Use dedicated, sealable containers
Further action needed to reach consensus
Comments

## Slide 8: Dispensary: Dose formulation accountability procedures
Consensus recommendation
  Control/test material containers weighed before and after contents removed for formulation
  Reconciled with theoretical weight required
  Balance records retained with study records
Further action needed to reach consensus
Comments
  Are there situations where this does not make practical sense (eg. multiple vials of pre-weighed material)

## Slide 9: General Principles: Dedicated equipment (e.g.glassware/vessels) for study and group
Consensus recommendation
  Wherever practical, separate equipment for controls and dose groups
  Dose pots should be study and dose group-specific then discarded
Further action needed to reach consensus
Comments
  Impact of trace contamination of glassware etc probably very low in terms of control animal exposure

## Slide 10: General Principles: Protective clothing and personnel hygiene procedures
Consensus recommendation
  Formulation lab
    Test materials handled in containment cabinet
    Formulations prepared and handled in ascending order
  Animal rooms
    Procedures in ascending order or change gloves and aprons between groups
      Change gloves if any evidence of contamination
Further action needed to reach consensus
  Cross reference procedures for radiolabelled work
Comments

## Slide 11: General Principles: Equipment, room cleaning and monitoring procedures
Consensus recommendation
  Cleaning requirements should be determined based on consideration of physicochemical/other properties of the test compound
  Effectiveness of cleaning procedures evaluated if reasons for concern
    Eg. previous experience, physicochemical properties

## Slide 12: General Principles: Equipment, room cleaning and monitoring procedures
Further action needed to reach consensus
  Equipment for making formulations and within animal room
    How is cleanliness verified?
    Swab before each new formulation/study
    Validate cleaning process against series of molecular classes?
      Some compounds may be more resistant, or assay LOQ may be very low
  Cleaning of workstation, balances, stirrers etc
    Same as above or different?
Comments
  Information required to assess cleaning requirements should be supplied with test material

## Slide 13: Animal room: Housing of animals (distribution of cages on racks, location of controls etc)
Consensus recommendation
  Separate racks for control and test animals preferable; if on same rack
    Block distribution, with gap between groups (for rodents)
  For some studies (eg. inhalation, diet) may prefer a control in separate room
  Use of enrichment items – cleaning, storage
    Group-specific and disposable
  How are large animals exercised – controls separate, treatment groups together (by sex)
  Anticipate risk of spread of contamination by urine/faeces
Further action needed to reach consensus
  Influence regulatory view on controls in separate rooms
  Share with regulators practical difficulties in large animal studies

## Slide 14: Animal room: Identification of dose formulations
Consensus recommendation
  Use of appropriate cross checking
    Eg. appearance, label, colour coding (labels, stirrers), cross check of dose pot weight, bar code
Further action needed to reach consensus
Comments

## Slide 15: Animal room: Dose formulation accountability procedures
Consensus recommendation
  Check use of formulation against theoretical requirement, eg. weigh each container before and after dosing (SG correction if necessary)
    Unexplained discrepancy of >10% triggers investigation
Further action needed to reach consensus
Comments

## Slide 16: In-life: Sampling of biofluids (equipment, gloves, workstations, storage of samples etc)
Consensus recommendation
  Sample tubes and paperwork prepared in separate, clean environment
  Sample tubes in sealed bags, by dose group; supply and open sampling equipment only as needed
  Careful consideration of sample site according to route of administration (eg. no orbital sinus bleeding in inhalation studies, clean rat tails for tail bleeding)
  Where possible, sample in (clean) area separate from animal holding
  Where possible controls sampled in separate area from treated animals; if not, controls sampled first, then ascending group order

## Slide 17: In-life: Sampling of biofluids (equipment, gloves, workstations, storage of samples etc) 2
  Dedicated bleeders, handlers etc
  Dedicated equipment for control and treated animals (eg. anaesthesia, warming cabinets, centrifuges etc)
  If not working in ascending order, or if visible contamination, change gloves, aprons between groups
Further action needed to reach consensus
Comments

## Slide 18: Necropsy: Sampling of biofluids/tissues (equipment, gloves, workstations, storage of samples etc)
Consensus recommendation
  Where TK samples taken at necropsy (mice, non-rodents), dedicated bleeder and controls first, dedicated equipment per group (necropsy equipment, cryobaths for tissue, homogenisers)
Further action needed to reach consensus
Comments

## Slide 19: Toxicokinetics: which studies, sampling times and sampling frequency for control animals
Consensus recommendation
  Both the bioanalytics and toxicology working groups addressed the issue of toxicokinetic sampling times and frequency and analysis of control samples. The following consensus was reached in plenary:
  The primary purpose of toxicokinetic data is to demonstrate exposure in treated animals rather than providing a quality control mechanism to demonstrate absence of exposure, which would have additional statistical implications.
  Other procedures are in place to ensure absence of exposure of control animals and these best practice recommendations are intended to improve these procedures to minimise as far as possible the potential for detecting drug in samples from control animals

## Slide 20: Toxicokinetics: which studies, sampling times and sampling frequency for control animals
Consensus recommendation
  Whilst recognising that the primary purpose of toxicokinetic data is to demonstrate exposure in treated animals, the workshop participants agreed that for pivotal studies in rodents/rabbits, at least 3 samples in a 24 hour period (tmax, t24h and one other timepoint) will be analysed from satellite animals. Control samples will be collected from control dogs with the same frequency as for treated dogs, and at least 3 control samples will be analysed for drug levels. It would be a company decision to do more than this proposed minimum if they so wished.

## Slide 21: Bioanalytics breakout session feedback

## Slide 22: Analysis of Dose Formulations: Sampling methods (gloves, equipment etc.)
Consensus recommendation
    Control Vehicle should be analysed, same day/week as TK Bleed
    Control diet sampled from jar in animal room (checks air-born contamination) FDA recommendation
Further action needed to reach consensus
Comments

## Slide 23: Analysis of Dose Formulations: Methods, assays and sequence of analysis
Consensus recommendation
    All samples handled the same way with validated methods
Further action needed to reach consensus
Comments

## Slide 24: Analysis of Biofluids/Tissues: Labelling and shipping
Consensus recommendation
    All samples (including controls) should be stored and shipped in conditions that minimise potential contamination and deterioration during transit (e.g tubes frozen in upright position, not overfilled).
    Samples bagged/separated by dose-group.
    Use of labels that withstand storage and remain legible to avoid mis-identification.
    Adequate and clear paperwork with dosing/sampling times
Further action needed to reach consensus
Comments

## Slide 25: Analysis of Biofluids/Tissues: Methods/equipment and sequence of analysis
Consensus recommendation
  Method validation should quantify and minimise carry-over issues/check selectivity in the same matrix as the study samples.
  Sample analysis should also include sufficient number of blanks to check for analytical contamination (in line with FDA Bioanalytical Guidance)
  Acceptable to analyse samples in ascending dose-group (bioanalysts have access to randomisation).
  Follow clean analytical work practises.
Further action needed to reach consensus
Comments
  Use same instrumentation/process for analysing controls and dosed samples - this was inconclusive
  What is an acceptable limit for carry-over ?
  Must always request enough sample volume for at least 2 analyses.

## Slide 26: Analysis of Biofluids/Tissues: Assay performance / LOQ
Consensus recommendation
    Methods should be validated (3-run including specificity) before Regulatory TK studies
    LLOQ should be set by dose-level and sample volume available (to assess exposure at NOEL, if technically possible)
Further action needed to reach consensus
Comments
  Need to define exposure at NOEL (may not always be able to do this with I/h or potent drugs)
  Use dose-range finder study to set LLQ/range.
  Definitive method available for first regulatory TK study

## Slide 27: Additional recommendations

## Slide 28: Reporting: Discussion of issue and study validity in study reports
Consensus recommendation
  Data related to detection of drug in samples from control group should be presented in the TK report
  TK report should address the levels of drug in samples from controls relative to the LLOQ and to the levels in treated animals
  Where drug is detected in samples from control group animals (above LLOQ) , this should be discussed in the text of main study report. Comment whether values near LLOQ, or well above
  Include statement of possible cause of contamination, if data indicates, no speculation. Cross refer to any on-going investigation
  In report Conclusion/Discussion: Impact on study integrity and validity of interpretation addressed, even when there is no negative impact

## Slide 29: Assessment of GLP compliance of study when drug detected in control samples
Consensus recommendation
  Statement of GLP compliance does not have to be qualified when drug is detected in samples from control group animals
  The detection of drug in samples from control group animals must be mentioned in final report, in order to be in compliance with FDA GLPs that require the final report lists ‘all circumstances that may have affected the quality or integrity of the data’
  If the presence of drug in samples from control group animals is determined to be the result of a mis-dosing, a protocol deviation should be noted.
Comments
  QA is responsible to assure that the report “accurately and completely reflects the raw data”, so they must assure that the detection of drug in samples from control group animals is reflected in the report
  Training of study personnel in measures/procedures to minimise contamination should be documented

## Slide 30: Follow-up measures when drug detected in control samples
Consensus recommendation
  SOP should be in place which describes process when drug is measured in a control sample
    Re-analyse when sample volume permits, following internal procedures and FDA guidance
    Check that analytical blanks (& plasma from unrelated control animals) are clean from contamination
    Check tube labelling and data/documentation provided with the samples
    Inform the study director as soon as positive result is confirmed [FDA GLPs require that the study director assure “unforeseen circumstances that may affect the quality and integrity of the nonclinical laboratory study are noted when they occur…” ]
Comments
  Assay for presence/absence of metabolites may aid in determining source of contamination

## Slide 31: Assessment of validity of studies for human risk assessment
Industry have recommended best practices to reduce the risk of detecting drug in control samples, but it is not a realistic expectation that it will be possible to eliminate this occurrence
Industry experience indicates that it is often not possible to identify the source, and/or fully correct the cause of drug in controls during the conduct of a study
Therefore a scientific weight of evidence approach is needed to evaluate the validity of the study data in assessing risk to humans

## Slide 32: Back-ups

## Slide 33: Toxicokinetics: which studies, sampling times and sampling frequency for control animals
Consensus recommendation – Tox breakout
  All pivotal toxicology studies
  Consider including earlier studies for “early warning”
  For (rat) repro studies, can extrapolate from existing data, assuming no change in procedure and no concerns
  Same sample points as for treated animals, analyse tmax, analyse other time points only if contamination detected
  If no contamination, consider more limited control analysis at subsequent time points/further studies
  Not necessary to sample control animals on same day as treated animals
Further action needed to reach consensus
Comments
  There may be other ways to monitor controls, using fewer animals

## Slide 34: Toxicokinetics: which studies, sampling times and sampling frequency for control animals
Consensus recommendation – Bionalytics breakout
  Collect control samples (same times as dosed animals) for all pivotal studies, specifically carc (rodents) and pivotal repro (at least).
  For some types of cpds/dosing regimens (I/halation), consider bleeding control gp on a different day.
  TK bleeds same day/week as Dose Concentration Analysis (vehicle control)
Comments
  collect same timepoints as dosed animals (satellites if appropriate), analyse Cmax only or all control samples. Still common (especially CRO studies), for control samples to be taken but not analysed (sponsor decides)
  Sampling times set in discussion with bioanalytical gp ?
  Analysis of controls from early studies may help develop methodolgies/id problems for later studies.
  Lack of histo does not mean analysis unnecessary
  Sampling frequency - to look or not ? How many times through a study - can be re-assuring.
  50:50 on taking a predose (zero hr) from dosed animals - depends on blood volume. For, adds confidence, Against use of animals/cost-benefit analysis.

## Slide 35: Follow-up measures when drug detected in control samples
Consensus recommendation – bioanalyytics breakout
    Positive controls re-analysed according to pre-defined criteria (FDA Guidance driven)
    Check analytical blanks are clean for carry-over/other contamination
    Check tube labelling and raw data documentation
    Communicate to Toxicology Study Director as soon as confirmed
Further action needed to reach consensus
Comments
  May investigate potential metabolites (investigation with Tox)